## Slide 1: eXtend Collection Tree Protocol
Bruno P. Santos¹
with
Marcos A. M. Vieira¹
Luiz F. M. Vieira¹
¹Universidade Federal de Minas Gerais, Brazil.

## Slide 2: Communication paradigms on wns many-to-one, one-to-many, and any-to-any
Anycast route to the sink(s)
  Used to data collection from the network
Problem
  Impossible check data delivery
Sink
Notes: First two paradigms allow the collection and dissemination of data respectively. However, with routing on
only one direction, it is infeasible to build reliable mechanisms to ensure the delivery of data end-to-end.

## Slide 3: Communication paradigms on wns many-to-one, one-to-many, and any-to-any
Propagating or Anycast routes from Sink to nodes
  Used to data dissemination in the network
  Reconfigure nodes
Problem
  Impossible check data delivery
  How create unicast routes for dissemination?
Sink
Notes: First two paradigms allow the collection and dissemination of data respectively. However, with routing on
only one direction, it is infeasible to build reliable mechanisms to ensure the delivery of data end-to-end.

## Slide 4: Communication paradigms on wns many-to-one, one-to-many, and any-to-any
Propagating or Anycast routes from Sink to nodes
  Used to data dissemination in the network
  Reconfigure nodes
Problem
  Impossible check data delivery
  How create unicast routes for dissemination?
Sink
Notes: First two paradigms allow the collection and dissemination of data respectively. However, with routing on
only one direction, it is infeasible to build reliable mechanisms to ensure the delivery of data end-to-end.

## Slide 5: Communication paradigms on wns many-to-one, one-to-many, and any-to-any
More generic paradigm
  Enable unicast routes between any pair of nodes
Problem
  Adds more complexity
  Requires large amounts of memory to storage routes
    sometimes impractical in wns
Sink

## Slide 6: eXtend Collection Tree Protocol (XCTP)
An extension of the Collection Tree Protocol
XCTP create reverse path enabling
  Sink to nodes
  Nodes to sink
XCTP requires
  Low storage of states
  Very low overhead in packets
Sink

## Slide 7: Prior work
Directed Diffusion,
DRIP, DIP, DHV,
Deluge
Many-to-one
(Collection)
Unreliable
CTP, MultiHopLQI,
MintRoute
One-to-many
(Dissemination)
Unreliable
Any-to-any
Reliable
Hydro, RPL. AODV, DSR, Dymo
XCTP
Collection
Reliable
Notes: Directed Diffusion and DIP, DRIP, DHV are used for dissemination of small data packets in the network.
Deluge is a protocol that operates under the one-to-many paradigm, which has the objective to propagate large amount of data
CTP is the de-facto standard collection routing protocol for Wireless Sensor Network and his results are better the MultiHopLQI and MintRoute.
Hydro, RPL. AODV, DSR, and Dymo are P2P protocols.
Hydro and RPL use tables schemes to stoge routes for any node. RPL uses several messages types to create DAGs to routing messages. RPL uses requires control packets to create downward routes, XCTP
does not have this overhead since XCTP takes advantage of thedata packets.
AODV, DSR and Dymo floods the network with messages RREQ. DSR uses packet header to store the route path. AODV and DSR are keep routes in memory.
XCTP focus in creating unicast routes to exchange messages in both directions root-to-node and vice-versa. XCTP create the routes using DATA PACKETS instead CONTROL PACKETS.
XCTP also allows non utilized downward routes to be removed through TTL-based policy avoiding memory overhead to store states with peer-to-peer routes that are underutilized.

## Slide 8: XCTP Architecture
Router
Interface to upper layer
Forward table
Reverse table
Forwarder
Link Estimator
Link Layer
Control plane
Data plane
Notes: The XCTP architecture major changes are highlighted in yellow and bold font
To accomplish the task of forwarding packets also in the reverse direction of the standard CTP data flow, we had to modify CTP architecture by adding new features to the protocol rules as well as incrementing the packet format.
We also created a reverse flow table.
The CTP rules were modified at the data and control planes to react appropriately to the two main events:
Reverse flow: correct and efficient installation of the reverse flow rules;
Topological changes: nodes must appropriately react when loops occur or when CTP unicast routes change.
The Router module is responsible for filling the Forward and Reverse tables
The Forward module queries the Forward and Reverse tables, and determines any router inconsistencies to inform the Router module
Upper Layer module is the interface provided to implement components that utilizes XCTP.

## Slide 9: XCTP Packets
Data Packet
Acknowledgment Packet
Notes: To allow the navigation of the reverse data packet, we added a 16 bits packet field to the data packet to represent the address of the message destination.
All fields are present in CTP data packet, except by “Destination” field
We created Acknowledgment packet type. The New Features field 16 bits is reserved for future features.

## Slide 10: Outline
Collection Reliable
Reverse Flows
Topological Changes
Evaluation
Conclusion
Notes: XCTP create rules in data and control planes to react

## Slide 11: XCTP’s Reverse Flows
XCTP create reverse fluxes with
  Data Packet or
  Sink demand
Read tables to downward packets
  Neighbor (from Link Layer), Reverse, and Forward
Fields Reverse Flow Table
  addr dest (tree descendant 2+ hops distance)
  next hop
  Time To Live (TTL)

## Slide 12: XCTP Reverse Flows (CRUD)
CTP create tree route
Table starts empty
Node C send a packet
Node A intercept a packet From C to Sink
Reverse route installed
B
D
C
A
A :Reverse Table |  | 
Dest | Next Hop | TTL
A :Reverse Table |  | 
Dest | Next Hop | TTL
C | B | 10
Tree to Sink

## Slide 13: XCTP Reverse Flows (CRUD)
Sink send packet to C
Node A intercept the packet and read tables
  Neighbor table (Not found)
  Reverse Table (Found)
  Forward table
Node A send uncast message to B
B delivery to C
B
D
C
A
A :Reverse Table |  | 
Dest | Next Hop | TTL
A :Reverse Table |  | 
Dest | Next Hop | TTL
C | B | 10
Tree to Sink

## Slide 14: Outline
Collection Reliable
Reverse Flows
Topological Changes
Evaluation
Conclusion
Notes: XCTP create rules in data and control planes to react

## Slide 15: XCTP Reverse Flows (CRUD)
Data packets from D are routed by B
Occurs link changes
  Route quality or broken links
Reverse table is out-dated
  Update Next Hop to C
B
D
C
A
A :Reverse Table |  | 
Dest | Next Hop | TTL
D |  | 10
Tree to Sink
B
C

## Slide 16: XCTP Reverse Flows (CRUD)
There is a link failure causing loop
The reverse table is out-dated
  All entries are invalid
Actions
  XCTP remove all entries
  CTP ensure a new tree to sink
Reverse flows entries are reconstructed with new data packets
B
C
D
A
Tree to Sink
A :Reverse Table |  | 
Dest | Next Hop | TTL
D | B | 10
. . . | . . . | . . .
A :Reverse Table |  | 
Dest | Next Hop | TTL
Tree to Sink

## Slide 17: XCTP permits paradigm any-to-any
B wants to send data to C
  There is not direct route
  B send the packet in collect route
Node A query tables
  Neighbor table (Not found)
  Reverse Table (Found)
  Forward table
Then downward the packets
In worst case, the packets will go to the sink and towards C
B
C
A
A :Reverse Table |  | 
Dest | Next Hop | TTL
C | X | 10
Tree to Sink

## Slide 18: Transport layer over XCTP
We implement Transport Automatic Piggyback Protocol (TAP2)
TAP2 uses for error-control
  Piggyback
  Automatic Repeat-reQuest (ARQ)

## Slide 19: Outline
Collection Reliable
Reverse Flows
Topological Changes
Evaluation
Conclusion
Notes: XCTP create rules in data and control planes to react

## Slide 20: XCTP experiments
We made comparisons with different protocols
  AODV and CTP in TinyOS implementation
  RPL in implementation Contiki
We run experiments on TOSSIM
  10 different topologies
  10 simulation in each scenario
Parameter | Value
Base station | 1 center
Number nodes | 100
Radio range (m) | 100
Density (nodes/m²) | 10
N# experiments | 100
Bytes transmitted | 1024
Path loss exponent | 4.7
Power decay (dB) | 55.4
Shadowing Std Dev (dB) | 3.5

## Slide 21: XCTP evaluation goals
Reliable?
  Packets delivery to sink
Robustness?
  Presence of faults and Different topologies
Scalability?
  Memory for routes
Control Traffic
  Beacons to maintaining routes
Memory requirements
  code and initial tables

## Slide 22: XCTP evaluation Reliable, Robustness, Scalability, Control, Memory

## Slide 23: XCTP evaluation Reliable, Robustness, Scalability, Control, Memory
Experiment 1#
Insert network failure
5 active flows
Disable 25% of the nodes
AODV presents long time to react
XCTP reacts quickly
finding new routes
In some scenarios, ADOV took over 200s to finish
XCTP on average takes 25s to complete all transfers

## Slide 24: XCTP evaluation Reliable, Robustness, Scalability, Control, Memory
Experiment 2#
Insert network failure
50 active flows
Disable 25% of the nodes
XCTP presents low difference of the behavior with and without network failures.

## Slide 25: XCTP evaluation Reliable, Robustness, Scalability, Control, Memory
RPL always uses all entries in route table
5 flows AODV consumes almost 100% of the route table
82% less from the table than AODV for the same amount of flows
Dismiss requests for new routes
or
Disconnection between some routes
Uses TTL to remove under-utilized routes

## Slide 26: XCTP evaluation Reliable, Robustness, Scalability, Control, Memory
XCTP
operates under the Reverse Table limit
XCTP is robust and scalable

## Slide 27: XCTP evaluation Reliable, Robustness, Scalability, Control, Memory
Control Traffic Overhead
Five-hours of experiments
XCTP sends fewer control packet than RPL
RPL needs additional beacons for create reverse routes

## Slide 28: XCTP evaluation Reliable, Robustness, Scalability, Control, Memory
 | CTP | RPL | XCTP | XCTP+TP2 | AODV | AODV + TAP2
RAM | 1505 | 6516 | 1812 | 1968 | 2119 | 2545
ROM | 16204 | 46454 | 17942 | 18435 | 13868 | 14562
XCTP add few pieces of code in CTP
≈ 1KB
XCTP requires small amounts of RAM
than AODV and RPL
Using TAP2
ADOV < XCTP < RPL

## Slide 29: Acknowledgment
We would like to thank for their financial support
  CNPq
  CAPES
  Fapemig
  LG

## Slide 30: Acknowledgment
We would like to thank for their financial support.
Conselho Nacional de Desenvolvimento Científico e Tecnológico (CNPq)
Coordenação de Aperfeiçoamento de Pessoal de Nível Superior (CAPES)
Fundação de Amparo à Pesquisa do Estado de Minas Gerais (Fapemig)
LG

## Slide 31: Conclusion
We present XCTP a protocol for WSN
  Reliable, Robust, Scalable, Efficient
  XCTP create anycast routes sink-to-nodes and nodes-to-sink
Lessons
  It is possible save memory creating only necessary routes for WNS